## Slide 1: smart public restroom
Problem Definition and Design Thinking
about our project

## Slide 2: PROBLEM Users may leave the tap running longer than necessary when manually flushing the sink. This results in unnecessary water wastage, leading to higher water bills and environmental concerns in areas with water scarcity. Washing hands with water without using soap is more likely to harbor germs. Manual flushing relies on user behavior, which can be inconsistent. Some individuals may not flush the sink after use, leading to hygiene issues and potential blockages in the plumbing. Users may not be mindful of water conservation, leading to excessive water use. This can be particularly problematic in public restrooms, where many people use the facilities throughout the day.
Solutions
To over come the above problems we can use the Sensors (infrared, ultrasonic, or other types),Microcontroller or programmable logic controller (PLC) or Arduino boards we can create the automated water flush with soup(liquid) systems for hand wash in sinks.

## Slide 3: PROBLEM With using latches or other type manual locks in the public restrooms or toilets are having lot of issues like Misalignment, Sticking or Jamming Loose Screws or Hardware ,etc... Opening the seat cover of the western toilets in empty hands is a ways to spreading infectious disease. In some public restrooms doors of the toilets are improperly locked or damaged.
Solutions
Using the below electronic components we can overcome the above problems.
Arduino board (e.g., Arduino Uno) and microcontrollers
Servo motor
Push button
Jumper wires
Electronic Door Lock
If the people enters the toilets by pressing push button to open the door automatically seat cover of the western toilet will be opened during the action of door opening.
If the people into the toilet automatically the door will be closed. Then they thought to leave from the toilets press the push button attached to open the door and to close the seat cover. When the closing of the seat cover after which time frame we need to flushing the water into the toilets it can be achieved by using above components.

## Slide 4: PROBLEM Flushing toilets are one of the primary water consumers in public restrooms. Urinals are often found in men's restrooms and also consume water when flushed. Handwashing is essential for hygiene and typically requires both hot and cold water.
Solutions
Some public restrooms are equipped with automatic-flush toilets and urinals. These fixtures use sensors to determine when to flush, which can help conserve water by preventing unnecessary flushing.
It can be this is only possible if there is water in the water tank, Without water we cannot use the toilets and restrooms for any purpose so, using the water level sensors, electronic door locks and arduino boards we can lock the doors of restrooms and toilets when the Amount of water is below the limit.
If the amount of water is more than specified limit doors will be opened automatically.

## Slide 5: PROBLEM Unpleasant odors can arise due to poor ventilation, inadequate cleaning, or issues with plumbing and drainage. Room temperature of the restroom will be rising at summer seasons.
Solutions
To help keep public restrooms smelling fresh at all times, we can add fragrance or air freshener dispensers to these spaces. This will help keep the restrooms feeling clean and welcoming no matter what time of day it is.
Use the air Fragrances for welcomes the people into the smart public restrooms ,flush the smell fragrances automatically in the specified time limit.
Using temperature sensors, relays and exhaust fans we can control the room temperature of the restroom

## Slide 6: PROBLEM Most of the peoples are not flush the water after using the restrooms particularly after the usage of urinals.
Solutions
We will using the motion sensors & Arduino board to flush water in the urinals after the usage of restrooms.

## Slide 7
Thank you